HP48 feature list

Alonzo Gariepy has pointed out to me that people might like to see 
a list of HP 48SX features, sent out by the firmware design team 
leader, Bill Wickes, to the reviewers before we got the calculators 
themselves. Here is a copy of that list. Many thanks, Alonzo and Bill.

Wlodek Mier-Jedrzejowicz,
Space Physics, Imperial College, London
BITNET: MIER @ SPVA.PH.IC.AC.UK
Disclaimer: This information is presented as is. NO CLAIMS about
its sutitability for any purpose are made by HP, my employers or 
myself. It is simply a copy of a private communication whose author 
has allowed me to make it available to a wider audience.
----------------------------------------------------------------------

Here's a slightly edited, although still not exhaustive list of features
(in no particular order) that I made recently:

			   HP-48SX Feature Summary

Hardware
	7.1"x3.2" footprint with tapered .7" - 1.1" thickness 
	single vertical format 49-key keyboard
	64 x 131 pixel STN LCD display
	256K ROM, 32K RAM built in
	Saturn CPU @ 2MHz (note--throughput ~1.5MHz compared to 28S @1MHz)
	2 memory card ports
		--battery backed RAM (32K or 128K)
		--ROM or OTP (OneTime Programmable)
	Bidirectional IR I/O at 2400 baud
	Wired serial port at 1200, 2400, 4800, 9600 baud
		cables available for IBM or Apple computers (~$35)
	3 AAA cells
	List price $350
	Two part-manual (800p) plus quick reference guide
	Brushed nylon case with velcro fastening, pocket for cards and guide

Firmware 
(Most HP 28 features not explicitly mentioned are included; "new" means "in
addition to that provided by the HP 28S.")

	HP-28-style multi-object-type RPN calculator, superset of 28 language
	Interactive stack environment, for point-and-shoot stack operations
	Prompts and menus to help beginners
	Coexistent graphics and stack/edit display memory
		Graphics display can be larger than physical display,
		with hardware scrolling
	2-dimensional graphical entry and display of algebraic expressions
	Spreadsheet-like matrix editor
	Redefinable keyboard
	Real-time clock & date display
	ECMA94 character set, 3 display font sizes
	Appointment and control alarms
	Plotting features:
		Eight types of automatic plots:	function, polar, 
                        conic sections, parametric, "truth", scatter, 
                        bar charts, histograms
		Autoscaling option
		Interactive plot environment
			zoom conrol, recentering, cursor readouts, labelling,
			etch-a-sketch, line & circle drawing, 
                        copying and erasing
			integration, differentiation, root-finding
	Graphics features:
		Dot and line drawing 
		Boxes and Circles
		Graphics objects of any size
		OR or XOR superposition
		Sub-region extraction
		Pixel or logical addressing
	Unit Management
		"Unit objects"--real numbers with physical dimensions
			allowed in algebraic expressions
		Automatic unit conversion in unit object operations
			arithmetic, integration, plotting, solving
		Interactive unit menus for simple conversions
	I/O
		Kermit protocol built in for calc-to-calc (IR) or 
                        calc-to-calc (serial)
		Server mode
		Low level serial commands
		Print to serial or IR
	Plugin Management
		Merged or independent RAM (max RAM 288K)
		Automatic menu of plugin applications and commands
		Archiving and restoring (also via I/O)
	Mathematics
		Common transcendentals on hard keyboard
		New:
			Symbolic integration (pattern matching)
			Summation function
			Programmable pattern match/replace
			"Where" function for sticky local variable bindings
			Generation of user-defined functions from 
                            algebraic assignments
			decimal to rational fraction conversion
	New supported object types:
		Graphics (replaces HP28 graphic strings)
		Tagged (for labeling objects)
		Unit
		XLIB Name (plug-in command)
		Directory
		Library (plug-in application/commands)
		Backup	(Independent RAM variable)
		Library Data (for use by plug-in applications)
	New programming features:
		CASE structure
		Programmable OFF and CONT
		Autostart for single step; step through subroutines
		Memory size and checksum for objects
		INPUT command (programmable command line)
		PROMPT (HALT with display string)
		Wait-for-key with timeout
		Custom error generation
		One-key typing aids for entire structures
		Extended custom and solver menu control
		Increment and decrement (variable) commands
		Storage arithmetic for all object types
		Global variable commands extended to local variables
		Decompile stack objects into command line

Wlodek Mier-Jedrzejowicz