ODIPKT(8)                                               ODIPKT(8)

NAME
        odipkt - translate Open Data-Link Interface to Packet Driver interface

SYNOPSIS
        odipkt [ logical_board [ vector ] ] 
        odipktpn [ logical_board [ vector ] ]
DESCRIPTION

        Odipkt.com provides a Packet Driver API over Novell's Open Data-Link 
        Interface, allowing a single network adapter to service IPX, tcp/ip, 
        and other protocol stacks which use packet drivers. Odipkt.com understands
        Ethernet, Token Ring, and ARCnet frame types. Ethernet and Token Ring frames 
        are passed unchanged to packet driver applications, but ARCnet frames are 
        internally mapped to Ethernet. Thus, packet driver applications do not need 
        specific knowledge of ARCnet in order to operate in such environments.

        The logical board argument indicates which logical adapter odipkt should 
        bind to. Under ODI, there is one logical adapter per frame type. There may 
        be multiple physical adapters, and multiple frame types per physical adapter. 
        The logical adapter number starts at zero and increases by one for each frame
        type. For example, if a system contained two physical adapters with two frame 
        types each, there would be four logical adapters numbered 0-3. The frame types
        are specified in the NET.CFG file which must be in the current directory 
        (or on the APPEND path) when the ODI drivers are loaded.

	Typically, the frame type used by default by Netware on a given adapter will 
	not be appropriate for tcp/ip. The correct frame type for tcp/ip on Token Ring 
	is TOKENRING_SNAP and the correct frame type for tcp/ip on Ethernet is almost 
	always ETHERNET_II. Assuming an existing installation with one adapter running
	the default Netware frame type, it will usually be necessary to define a second
	frame type (as listed above) and to specify the logical board argument as 1.
        An exception to this rule is ARCnet which uses only one frame type. Below 
        is a NET.CFG entry for a 3c501 using the default address and interrupt. 
        Other Ethernet adapters would use similar configurations:

        Link driver 3c501 
              envelope type ETHERNET_802.3 
              envelope type ETHERNET_II

	Given the above entry, the logical board argument of oipkt would be 1. 
	Token Ring uses different frame types:

        Link driver token 
              envelope type TOKEN-RING 
              envelope type TOKEN-RING_SNAP

	Again, the logical board should be specified as 1 for this example. ARCnet 
        installations require no frame-type definitions and should use a logical board
        of 0.

        Because odipkt.com uses buffers provided by the Link Support Layer, the Link
        support section of NET.CFG must specify at least one buffer of a size 
        appropriate to the medium in use. Some adapters require more buffers for 
        optimal performance, e.g., the 3c503 can use at least five during reception 
        of back-to-back packets. The following lines configure five buffers large
        enough for Ethernet:
	
	Link support
	      Buffers 5 1600

        The correct buffer size for Token Ring will vary depending on the installation.
        Specifying too small a buffer size will result in unpredictable behavior.
	
	Vector is the packet driver interrupt at which to provide service. The default
	is 105 and the parameter is decimal.

	Odipkt.com should be loaded after lsl.com and the adapterspecific driver(s). 
	It must, of course, be loaded before the packet driver applications which use 
	it. The Netware shell and ipxodi.com can be loaded before or after the 
        odipkt.com program.

        Odipktpn.com supports an older version of the ODI specification as used in
        Farallon's PhoneNET Talk product. Operation of opipktpn.com is identical to
        that of opipkt.com but configuration of NET.CFG is somewhat different: no
	''envelope'' statements are required or allowed. Because multiple frame types 
        are not supported, odipktpn.com treats all Ethernet cards as ETHERNET II.

AUTHOR 
	Dan Lanciani 
	185 Atlantic Road 
	Gloucester, 
	MA 01930