Path: funic!fuug!mcsun!uunet!wuarchive!sdd.hp.com!hp-pcd!hpcvra.cv.hp.com!rnews!hpcvbbs!akcs.burhan
From: akcs.burhan@hpcvbbs.UUCP (burhan h. afandi)
Newsgroups: comp.sys.handhelds
Subject: Re: copy-rom.lib
Keywords: copy rom
Message-ID: <2876c534:3606.2comp.sys.handhelds;1@hpcvbbs.UUCP>
Date: 7 Jul 91 07:40:07 GMT
References: <286f60d3:3606comp.sys.handhelds@hpcvbbs.UUCP> <286f6916:3606.1comp
Lines: 92


                Copy-rom is a library which inables you to copy ROM to
             RAM .
             You can send the content of a ROM card directly to a pc for
             storage, or copy the  content to a port on your calculator.
             COPY-ROM allows You to copy an entire port(ROM or RAM) or
             just a selected number of files.
              
             ==========STORAGE ON A COMPUTER DISK=============
              
             (COPY TO PC) COMMAND:->->PC
              
              
             if the argumen is a number (0,1 or 2)the entire given port
             is coppied.
             if the argument is a library identifier (:port#:library#)
             only the identified library is coppied.
             if the argument is a list of library identifiers, only the
             files in the list are coppied.
              
              
             ===========COPY TO STACK=====================
              
              
             (COPY TO STACK) COMMAND: STK/|\
                                          |
              
             This command takes the same arguments as ->->PC, however,
             the result is returned to stack.
              
              
             ==============COPY TO PORT===================
              
              
             (COPY TO PORT) COMMAND: /|\PORT
                                      |
              
             This command takes an additional argument in level one which
             is the port# to which you want to copy the files.
             So this command takes two arguments:
             the level two argument may be a library
             identifier(:por#:library#) or
             a list of library identifiers or
             a port#(0,1 or 2).
             the level one argument must be a number (0, 1 or 2)(this is
             the port number to which you want to copy the files)
              
             EXAMPLE: Let us assume that we have a ROM card in por #2 and
             we want to copy this ROM card to a RAM card located in port
             #1.
              
             solution:
              
             simply Enter the source port (2)
                    then the destination port(1)

                    implement /|\port to copy port 2 to port one
                               |
              
             summary:
              
              
                      2 [ENTER]
              
                      1 [ENTER]
              
             Now press the key labeled { /|\PORT }
                                          |
             now the content of port 2 is coppied to port 1.
              
             This command also accepts a list containing two port #s as
             an argument.
              
             in the above example we could also have entered {2 1} as an
             argument where the first element of the list is the source
             por# and the second is the destination port#.
              
              
             ==============ATTACHING COPY-ROM=================
              
             Cut and transfer the library to your calculator, store it
             under any name.(make sure it is stored under the first menu
             key of VAR menu) execute the program.
             COPY-ROM.Lib will appear on the stack.
             store it in a port as follows:
              
             :port#:1424    [STO]
              
             Turn your calculator off and then ON, the library will
             attach itself.